## Slide 1: Project 2: Random Access Procedure in MAC
Notes: https://pixabay.com/photos/building-city-business-office-4803602/

## Slide 2: Table of contents
01
02
03
04
05
06
MAC
Introduction to MAC Layer
MAC Architecture
Random Access Procedure
Code
Output
Conclusion

## Slide 3: About
The Random Access Procedure in the Medium Access Control (MAC) layer is a fundamental aspect of wireless communication systems. It is responsible for managing the initial connection establishment between a user device and the network, as well as controlling how devices access the shared communication channel.
This project focuses on the Random Access Procedure, which plays a critical role in ensuring that devices can efficiently and fairly access the communication channel. By implementing and testing various aspects of this procedure, the project aims to improve network performance, reduce latency, and optimize resource allocation, thereby enhancing the overall reliability and efficiency of wireless communication systems.

## Slide 4: Group members
Rajeshwari
Swetav
Sujata
Pavan
Prasad
Shashwat
Bhuvaneshwari
Mentor/Guide:
Abhijeet Kumar

## Slide 5: Mac
Introduction to MAC Layer

## Slide 6: MAC Layer
The Medium Access Control (MAC) layer is a fundamental component of the data link layer (Layer 2) in the OSI (Open Systems Interconnection) model, particularly in mobile communication systems like LTE (Long-Term Evolution), 5G NR (New Radio), and earlier technologies like UMTS (Universal Mobile Telecommunications System).
The MAC layer is responsible for managing how data is transmitted over the shared wireless medium, ensuring that multiple users can access the network efficiently and fairly.
The MAC (Media Access Control) layer is a sublayer of the Data Link layer in the OSI model.
It is responsible for controlling how devices on a network gain access to the medium and permission to transmit data.
3GPP 38.321,38.331

## Slide 7: Mac Architecture

## Slide 8
Fig 1.1 MAC Layer Architecture
4.2.2 of 3GPP 38.321

## Slide 9: FUNCTIONS AND SERVICES OF MAC LAYER
Functions
Mapping between logical channels and transport channels
Multiplexing of MAC SDUs
Demultiplexing of MAC SDUs
Scheduling information reporting
Error correction through HARQ
Logical channel prioritization
Services
Services provided to upper layers
data transfer
radio resource allocation.
Services expected from physical layer
data transfer services
signalling of HARQ feedback
signalling of Scheduling Request
measurements (e.g. Channel Quality Indication (CQI))
4.3, 4.4 of 3GPP 38.321

## Slide 10: Random Access Procedure

## Slide 11: Phases of the Random Access Procedure
The procedure typically involves four key steps:
Random Access Preamble Transmission:
  The UE selects a preamble, either randomly from a pool (CBRA) or based on network assignment (CFRA), and transmits it on the Physical Random Access Channel (PRACH). The preamble is a short signal that does not carry data but is used to request access.
Random Access Response (RAR):
  The network detects the preamble and responds with a Random Access Response message on the Physical Downlink Control Channel (PDCCH). This response includes timing advance information, a temporary identifier (Random Access-Radio Network Temporary Identifier, RA-RNTI), and uplink grant information, allowing the UE to send a message to the network.
Scheduled Transmission:
  The UE uses the granted resources to send a message, often referred to as the RRC Connection Request in the context of initial access, or a RRC Re-establishment Request if re-establishing a connection. This message is sent on the Physical Uplink Shared Channel (PUSCH) and includes information that helps the network identify the UE.
Contention Resolution:
  For CBRA, if multiple UEs have sent the same preamble, they may both receive the same RAR, leading to a contention scenario. The network sends a contention resolution message, which the UE uses to determine if it has successfully accessed the network. If successful, the UE proceeds with communication; otherwise, it will attempt the Random Access Procedure again.
5.1 of 3GPP 38.321

## Slide 12: Fig 2.1 Random Access procedure
4.2.2 of 3GPP 38.321
4.5 of 3GPP 38.321

## Slide 13
Random Access Procedure
Why and when random access is used?
Initial access from RRC_IDLE
RRC Connection Re-establishment procedure
DL or UL data arrival during RRC_CONNECTED when UL synchronization status is "non-synchronised"
Loss of UL Synchronization
SR failure
Request by RRC upon synchronous reconfiguration
Transition from RRC_INACTIVE
Request for Other SI
Beam failure recovery
Time alignment at scell addition
Fig 2.2Types of Random Access Procedure
5.1 of 3GPP 38.321

## Slide 14: C
There are two types of Random Access Procedures:
Contention-Based Random Access (CBRA):
The UE selects a random access preamble from a shared pool, risking contention with other UEs.
There is a chance that multiple UEs will choose the same preamble, leading to potential contention.
The Random Access Response (MSG2) provides uplink resource allocation for MSG3, and UEs choosing the same preamble will receive identical MSG2 content.
UEs transmitting MSG3 using the same MSG2 will use the same set of resource blocks and symbols.
Contention Resolution is handled differently based on the type of message: For CCCH messages, it uses a MAC Control Element in MSG4. For DCCH or DTCH data, it relies on C-RNTI for addressing and resolution.
The Base Station decodes one MSG3, identifies the successful UE, and informs it through MSG4, while other UEs must retry with a different preamble.
Contention-Free Random Access (CFRA):
Types of Random Access Procedure
The Base Station assigns a dedicated random access preamble to the UE, eliminating the risk of contention.
Since the preamble is uniquely allocated, there is no possibility of contention.
The Random Access Response (MSG2) provides specific uplink resource allocation for MSG3 based on the dedicated preamble.
3GPP 38.221, 38.212, 38.213
3GPP 38.101-1, 2, 38.521-1

## Slide 15
Fig 3.1 CBRA procedure
Fig 3.2 CFRA procedure

## Slide 16
Table 3.1 CBRA vs CFRA comparison
Table 3.2 RACH Trigger Scenarios in NSA vs SA

## Slide 17: Code

## Slide 18
Code
Source: GitHub, LinkedIn

## Slide 19: Code Output

## Slide 21: Thank You!
From Team 4:
Rajeshwari
Swetav
Sujata
Pavan
Prasad
Shashwat
Bhuvaneshwari