## Slide 1: 5G NR Physical Uplink Share Channel (PUSCH) Signal Processing
PROJECT 5:

## Slide 2: Table of Contents
Introduction to 5G NR PUSCH​
Role of 5G NR PUSCH ​
Signal Processing in PUSCH​
Code​
Output​
PUSCH Signal Processing Group 4

## Slide 3: Group Members
Rajeshwari
Swetav
Sujata
Pawan
Prasad
Shashwat
Bhuwaneshwari
Mentor/Guide:
Abhijeet Kumar
PUSCH Signal Processing Group 4

## Slide 4: About Project
This project offers a comprehensive analysis of the Physical Uplink Shared Channel (PUSCH) within 5G networks, focusing on its pivotal role in facilitating uplink communication by transmitting both user application data and signaling messages. By delving into the intricate signal processing tasks associated with PUSCH, the project underscores its essential function in achieving high-speed data transmission and optimizing network performance. The versatility of PUSCH is also highlighted, demonstrating its ability to meet the diverse demands of various users and services in a dynamic network environment.
PUSCH Signal Processing Group 4

## Slide 5: Introduction to 5g nr pusch
PUSCH Signal Processing Group 4

## Slide 6: Physical Uplink Shared Channel
The Physical Uplink Shared Channel (PUSCH) is used to transfer end-user application data and Signaling Radio Bearer (SRB) messages. Application data belongs to the user plane, while SRB messages belong to the control plane.
The PUSCH can be used to transfer control information generated by the set of radio network protocol stack layers. For example, the MAC layer can add a range of MAC Control Elements (MAC CE) including Buffer Status Reports and Power Headroom Reports. The MAC Control Elements which can be transferred using the PUSCH.
A UE can transmit the PUSCH using either a CP-OFDM or DFT-S-OFDM waveform (it is mandatory for all UE to support both waveforms).
The PUSCH can use the π/2-BPSK, QPSK, 16QAM, 64QAM and 256QAM modulation schemes. The π/2-BPSK modulation scheme is only permitted when Transform Precoding is enabled, i.e. when using the DFT-S-OFDM waveform. It is a low order modulation scheme with a low PAPR so helps to improve coverage.
3GPP 38.211
PUSCH Signal Processing Group 4

## Slide 7: Role of 5g nr pusch
PUSCH Signal Processing Group 4

## Slide 8: Role of Pusch in 5g
Essential for Uplink Communication: PUSCH is the backbone of uplink communication in 5G, without which user data could not be reliably transmitted to the network.
Enabling High-Speed Data: It supports the high-speed data transmission that is a hallmark of 5G, enabling services like HD video streaming, real-time gaming, and more.
Adaptable to Diverse Requirements: The flexibility of PUSCH allows it to meet the varying demands of different users and services, from low-power IoT devices to high-bandwidth mobile users.
Contributing to Network Efficiency: By enabling efficient use of uplink resources, PUSCH plays a key role in maximizing the overall efficiency and performance of the 5G network.
PUSCH Signal Processing Group 4

## Slide 9
Enter your text here
Fig 2.1 Overview of PUSCH Uplink Modulation and Transmission Process
PUSCH Signal Processing Group 4

## Slide 10: PUSCH (Physical Uplink Shared Channel)
The physical-layer model for Physical Uplink Shared Channel transmission is described based on the corresponding PUSCH physical-layer-processing chain. Processing steps that are relevant for the physical-layer model, e.g. in the sense that they are configurable by higher layers, are highlighted in blue.
- Higher-layer data passed to/from the physical layer
- CRC and transport-block-error indication
- FEC and rate matching
- Data modulation
- Mapping to physical resource
- Multi-antenna processing
- Support of L1 control and Hybrid-ARQ-related signalling
3GPP 38.211
PUSCH Signal Processing Group 4

## Slide 11
Fig 2.2 Physical Layer model for UL-SCH transmission
PUSCH Signal Processing Group 4

## Slide 12: Signal processing in pusch
PUSCH Signal Processing Group 4

## Slide 13: Signal Processing in PUSCH
1. Transport Block CRC Attachment (TS 38.212 Section 6.2.1)
Purpose: A Cyclic Redundancy Check (CRC) is attached to the Transport Block to detect any errors during transmission.
Details:
  If the size of the TB is greater than 3824 bits, a 24-bit CRC is attached.
  If the TB size is less than or equal to 3824 bits, a 16-bit CRC is attached.
2. LDPC Base Graph Selection (TS 38.212 Section 6.2.2)
Purpose: Low-Density Parity-Check (LDPC) codes are used for error correction. The base graph selection is crucial for determining how the LDPC coding is applied.
Details:
  Base Graph 2 is selected if:
    The target coding rate is less than 0.25.
    The TB size is less than 292 bits.
    The TB size is less than 3824 bits and the coding rate is less than 0.67.
  Base Graph 1 is used for all other cases.
3GPP 38.212
PUSCH Signal Processing Group 4

## Slide 14
Fig 3.1 Physical layer processing in PUSCH
PUSCH Signal Processing Group 4

## Slide 15
3. Code Block Segmentation and Code Block CRC Attachment (TS 38.212 Section 6.2.3)
Purpose: If the Transport Block is too large, it is segmented into smaller Code Blocks, and a CRC is added to each segment to ensure data integrity.
Details:
  Base Graph 1: Segmentation is required if TB size + CRC > 8448 bits. The number of segments is calculated as Roundup((TB size + CRC) / (8448 - 24)).
  Base Graph 2: Segmentation is required if TB size + CRC > 3840 bits. The number of segments is calculated as Roundup((TB size + CRC) / (3840 - 24)).
  Each segment gets a 24-bit CRC attached.
4. Channel Coding (TS 38.212 Section 6.2.4)
Purpose: This step involves applying LDPC channel codes to each code block for forward error correction, making the transmission more robust against errors.
5. Rate Matching (TS 38.212 Section 6.2.5)
Purpose: Rate matching adapts the encoded data to fit into the available radio resources. This step ensures that the coded bits match the physical layer resources available for transmission.
3GPP 38.212
PUSCH Signal Processing Group 4

## Slide 16
Fig 3.2 Physical layer processing in PUSCH
PUSCH Signal Processing Group 4

## Slide 17
6. Code Block Concatenation (TS 38.212 Section 6.2.6)
Purpose: After rate matching, the segmented code blocks are concatenated back together to form
the final data stream to be transmitted.
7. Data and Control Multiplexing (TS 38.212 Section 6.2.7)
Purpose: This final step multiplexes the user data with control information (like HARQ acknowledgments and channel state information). The combined data is then mapped to the physical layer for transmission.
8. Scrambling (TS 38.211 Section 6.3.1.1)
Purpose: Scrambling is applied to the bit sequence to randomize the transmitted signal. This helps in reducing interference between users by making the transmitted data appear more random.
Details: The bits are XORed with a pseudorandom sequence generated based on a specific scrambling code, which varies for each user.
9. Modulation (TS 38.211 Section 6.3.1.2)
Purpose: The scrambled bits are then mapped onto modulation symbols. This converts the binary data into symbols that can be transmitted over the air.
Details:
  Modulation schemes such as QPSK (Quadrature Phase Shift Keying), 16-QAM, 64-QAM, and 256-QAM are used.
  The choice of modulation depends on the link quality; higher order modulations (like 64-QAM, 256-QAM) allow more data to be transmitted but require better signal quality.
3GPP 38.212, 38.211
PUSCH Signal Processing Group 4

## Slide 18
10. Layer Mapping (TS 38.211 Section 6.3.1.3)
Purpose: The modulation symbols are mapped onto multiple layers according to the MIMO (Multiple Input Multiple Output) configuration.
Details:
  Depending on the number of antenna ports (1 to 4 layers), the modulation symbols are distributed across these layers.
  Layer mapping allows the use of spatial multiplexing to increase data throughput.
11. Transform Precoding (TS 38.211 Section 6.3.1.4)
Purpose: Transform precoding is applied if the DFT-S-OFDM (Discrete Fourier Transform Spread OFDM) waveform is selected, which is typically used in uplink transmissions to improve the signal's resilience to frequency-selective fading.
Details:
  This step converts the time-domain symbols into frequency-domain symbols, spreading them across the available subcarriers.
12. Precoding (TS 38.211 Section 6.3.1.5)
Purpose: Precoding prepares the symbols for transmission by mapping them onto the antenna ports. It optimizes the signal for transmission based on channel conditions.
Details:
  Precoding adjusts the phase and amplitude of the signals on each antenna to improve signal quality and reduce interference.
3GPP 38.211
PUSCH Signal Processing Group 4

## Slide 19
Details:
  For CP-OFDM (Cyclic Prefix-OFDM) or DFT-S-OFDM waveforms, IFFT converts the frequency-domain data back into the time-domain signal, ready for transmission over the air.
  CP-OFDM is typically used for downlink and some uplink transmissions, while DFT-S-OFDM is used in uplink to provide additional robustness against channel impairments.
3GPP 38.211
PUSCH Signal Processing Group 4

## Slide 20
PUSCH Transmission: Codebook Based
Codebook based transmission means that the UE transmits the PUSCH using precoding weights have which been selected from a codebook standardized by 3GPP.
The Base Station provides instructions on the PDCCH regarding the choice of precoding weights that the UE must apply.
Code block CRC attachment
Fig 3.3 Codebook based PUSCH transmission
3GPP 38.212
PUSCH Signal Processing Group 4

## Slide 21
PUSCH Transmission: Non-Codebook Based
Non-codebook based transmission means that the UE measures a downlink CSI Reference Signal to generate its own precoding weights for the PUSCH. These precoding weights arc not constrained to a codebook standardized by 3GPP. Non-codebook based transmission relies upon channel reciprocity because the lJE determines its uplink precoding weights based upon downlink measurements
Once the Base Station knows the UE capability, it can instruct the UE to use non-Codebook based transmission using the txConflg information element within the PUSCH-Conflg parameter structure.
Code block CRC attachment
Fig 3.4 Non-Codebook based PUSCH transmission
3GPP 38.212
PUSCH Signal Processing Group 4

## Slide 22: Code
PUSCH Signal Processing Group 4

## Slide 23: Code
Source: GitHub, LinkedIn
PUSCH Signal Processing Group 4

## Slide 24: OUTPUT
PUSCH Signal Processing Group 4

## Slide 25: Output
PUSCH Signal Processing Group 4

## Slide 26: Thank you
PUSCH Signal Processing Group 4